## Slide 1: Lab 3
Figure 1:
car tail lights
L3 L2 L1 R1 R2 R3
L3 L2 L1
L3 L2 L1 R1 R2 R3
(c) Emergency
Note: Figures above are from John F. Wakerly, “Digital Design: Principles & Practices,” 3rd ed., Prentice Hall, 2000.
R1 R2 R3

## Slide 2: Note: below is NOT a complete state diagram
First, there are 3 input signals: E, L, R. Each state must have the transitions that cover all 23 = 8 combinations of inputs
E L R
0 0 0 E’L’R’
0 0 1 E’L’R
0 1 0 E’LR’
0 1 1 E’LR
1 0 0 EL’R’
1 0 1 EL’R
1 1 0 ELR’
1 1 1 ELR
allon
off
Ron1
Lon1
E’L’R
E’LR, EL’R’, EL’R, ELR’, ELR
E’LR’
E’L’R’
Observe that this transition from ‘off’ to ‘allon’ covers 5 input combinations
To make an easier to read state diagram, below is the outputs of each state
State L3 L2 L1 R1 R2 R3
Off 0 0 0 0 0 0
allon 1 1 1 1 1 1
Ron1 0 0 0 1 0 0
Lon1 0 0 1 0 0 0
It is your pre-lab 3 assignment to
complete this state diagram
Note: From the above state diagram, state ‘off’ is complete with all transitions